## Slide 1: A Unified Interface for Experimentation at the Edge Initial Thoughts
Srikanth Sundaresan
ICSI

## Slide 2: Measurements from the edge are critically important
Broadband is a critical resource
  Not a luxury anymore
View from the outside just as important as the view from inside
The edge is as complex as the core
  If not more – problems are devilishly difficult to pinpoint, let alone solve

## Slide 3: … Which explains why there are so many platforms
Project BISmark

## Slide 4: Do we need so many platforms?
 | BISmark | Ark | SamKnows | RIPE
Continuous active | Y | Y | Y | Y
Passive | Y | N | Y/N | N
Scope of experiments | High | Higher (better CPU/storage) | Medium(resource constraints) | Low (only use tools compiled in)
Heavy duty exp | ? | Y | N | Y/N
Local storage | N | Y | N | N
Scale | ~ | ~ | Y | Y
Each platform is unique, valuable in its own right

## Slide 5: As a researcher, what would one choose?
Considering experiment that can potentially run on all platforms:
  Scale
  Ease of deployability
Experiment deployability is important
  Else platform will never be used outside of niche group

## Slide 6: How easily are experiments deployable in current platforms?
BISmark – not difficult (?)
  Comfortable with openwrt
  Ash, C, lua
  Short turn-around times (weeks)
Ark ?
SamKnows
  Ash, C
  Long turn-around times (months)

## Slide 7: Can we write experiments once and deploy everywhere?
It’s complicated
  Technically possible
    Standard cross-compilation techniques
    A few hardware/other quirks (interface names, etc)
    Some effort in integrating with existing experimentation method
  More difficult in practice
    Memory / CPU / bandwidth / time constraints
    Need to make code general-purpose

## Slide 8: Case study: Porting WtF to SamKnows
Where’s the Fault
  Tool that localizes throughput bottlenecks to access link or wireless gateway
  Collects passive pcaps
  Proof-of-concept code in Ash + custom small C modules
  Extensively tested on BISmark
    65+ homes, 2 months
  FCC got interested in June 2013

## Slide 9: Timeline of porting WtF to SamKnows
Summer 2013
  Realized that Netgear 3500 has Broadcom chipset, which reduces functionality
  2/3 of nodes which has Atheros chipset is deployed off-path
Fall 2013
  Proof-of-concept code that works flawlessly in BISmark but fails miserably in SamKnows
Spring 2014
  Ported WtF as a lightweight, predominantly C-based program
Summer 2014
  Early testing + adding features
  Testing on 100 nodes (still larger than entire BISmark deployment)
Late summer 2014
  Initial deployment
  … which got postponed due to FCC MBA measurements cycle
Fall 2014
  Deployment!
  Wholesale crash of 30-40% of nodes within 36 hrs
  Experiment pulled (we did get some really interesting data though!)

## Slide 10: A unified experiment development platform
Is there a standard development platform we can agree upon and enforce?
  C/C++ with Shell/Lua
Some “basic” constraints / good habits
  Memory, CPU, storage, network utilization
  Real people may be using the network!!
Can we impose tight constraints and maintain usefulness of platforms?

## Slide 11: Keep management small and separate
Experiment vetting
  Does it meet ToS of platform?
  Security (hard!)
  Resource utilization (hard!)
  But likely only needs to be done on one platform
Constraints should be managed by experiment
  Hardware
    A wireless component that works on BISmark should fail gracefully on Ark
  Keep resource utilization minimal

## Slide 12: Basic assumptions
Simple packaging system
  Expecting users to figure out packaging for every single platform is expecting too much
    Openwrt makefiles are not pretty
  Give us a pointer to the code repo, we’ll generate the package
Package management system
  Pick nodes
  If the code repo updates, the deployments update

## Slide 13: BISmark and Ark
Probably easiest to integrate (externally, not internally)
  Similar (yet different) vision, platform
The researcher needs to provide
  Code that is platform-agnostic
The platform provider needs to provide
  Platform-specific package management
  Integration into experiment universe (crontab)
  Nodes
  Data pipeline

## Slide 14: So what should the platforms provide?
Maintain an open, easy-to-use development toolchain (easy)
  Keep platform-specific build management separate from code
Sync data
  Can be offline
Provide list of constraints (easy)
  Memory, CPU, network usage, time
Enforce constraints (hard)
  Sandboxing: very difficult, if not impossible to vet experiments or deploy without losing sleep

## Slide 15: Practical first step
Run basic experiments on each others’ platforms
  Bismark-active: periodically measures latency, throughput, packet loss, jitter
  Something light-ish from Ark?
BISmark  bismARK*
* This might not happen